## Slide 1
D2NN Loss Function Sweep
Static D2NN Practical Limits & Optimal Loss Strategy
2026-04-03 | FSO Beam Cleanup Research

## Slide 2
Experiment Overview
10 loss strategies across 3 sweeps, 2 datasets
Sweep | Data | Strategies | Status
0401 | dn100um (Lanczos) | PIB, Strehl, IO, CO+PIB | Complete
0402 | pitch_rescale | Abs Bucket (F), TP+PIB (B), Multiplane (C) | Complete
0403 | pitch_rescale | CO+hardTP, AbsBkt+CO, PIB+hardTP | In progress
10
Loss Strategies
5000
Training Pairs
30
Epochs Each
~6 min
Per Epoch (A100)

## Slide 3
Normalized PIB Lies
High PIB does NOT mean high received power
Strategy | PIB@10μm | Throughput | Abs Power vs Turb | Verdict
PIB Only (0401) | 90.1% | 50.7% | 58.7% | LOSS
Abs Bucket F (0402) | 81.4% | 98.6% | 105.8% | GAIN
TP+PIB B (0402) | 81.6% | 98.4% | 105.8% | GAIN
Multiplane C (0402) | 84.2% | 39.5% | 44.2% | LOSS
CO+hardTP (0403) | 74.0% | 99.3% | 97.0% | ~NEUTRAL
Key Insight: PIB Only achieved 90% PIB but absolute received power was only 58.7% of turbulent baseline. Throughput is the real metric.

## Slide 4
Why Does Throughput Drop?
1
Phase Mask Pattern
D2NN learns high-frequency phase gratings to redirect energy
2
Evanescent Waves
High spatial frequencies exceed propagation cutoff (k²x + k²y > k²)
3
Angular Spectrum Filter
Band-limited propagation zeros out evanescent components
4
Energy Lost
Turbulent beams lose MORE energy (50%) than vacuum (20-30%)
D2NN acts as a spatial filter — scatters unwanted energy away

## Slide 5
Absolute Received Power (0402)
Turbulent (gray) vs D2NN (color) — 500 test samples, bucket @10μm
Abs Bucket (F)
+5.8% vs turbulent
TP+PIB (B)
+5.8% vs turbulent
Multiplane (C)
-55.8% vs turbulent

## Slide 6
Throughput vs PIB: Structural Trade-off
PIB@10μm vs Throughput
Strategy | PIB@10μm | Throughput | Abs Power
PIB Only | 90.1% | 50.7% | 58.7%
Abs Bucket (F) | 81.4% | 98.6% | 105.8%
TP+PIB (B) | 81.6% | 98.4% | 105.8%
Multiplane (C) | 84.2% | 39.5% | 44.2%
CO+hardTP | 74.0% | 99.3% | 97.0%
Enforce TP
Scatter blocked → PIB limited to ~81%
(+5.8% absolute power)
Release TP
PIB reaches 90% but absolute
power drops to 59% of baseline
Fundamental Limit
Static phase masks cannot correct
random turbulence without energy loss

## Slide 7
Phase Mask Patterns
PIB Only (0401) — High-frequency grating, aggressive scatter
Abs Bucket (0402) — Nearly flat, throughput preserved

## Slide 8
Zernike Mode Analysis
Can D2NN correct wavefront aberrations while maintaining throughput?
Strategy | Higher-order Δ | Tip/Tilt Δ | Throughput | Assessment
F/B (Abs Bucket) | ±1 nm | ±0.2 nm | 98% | No WF correction
Multiplane C | -28 nm | +1.3 nm | 40% | Good WF, bad TP
PIB Only | -28 nm | +16 nm | 51% | WF + scatter
Dilemma:
Wavefront correction requires the D2NN to create complex phase patterns.
These patterns generate high spatial frequencies that get clipped by propagation.
Result: correcting wavefront = losing energy. A structural limit of static optics.

## Slide 9
CO Loss Alone Fails (0403)
co_hard_tp: CO + Quadratic TP penalty (λ=10)
99.3%
Throughput
Best of all strategies
74.0%
PIB@10μm
Below baseline (76.1%)
97.0%
Abs Power vs Turb
3% loss in received power
Why: CO optimizes full-field matching (amplitude + phase), not bucket concentration. No gradient signal to focus energy into the 10μm bucket.
Remaining hope: pib_hard_tp combines PIB concentration + TP enforcement

## Slide 10
Conclusions
1
Throughput is the real metric
Normalized PIB can be misleading. Only strategies with TP > 95% improved absolute received power.
2
Static D2NN limit: +5.8%
Best absolute power improvement over turbulent baseline (Abs Bucket / TP+PIB strategies).
3
PIB + TP are structurally opposed
Concentrating energy requires scattering → throughput loss. Static masks can't escape this trade-off.
4
Vacuum PIB (94%) is unreachable
With throughput maintained, maximum PIB is ~82%. Closing the gap requires fundamentally different approaches.

## Slide 11
Next Steps
Pending (0403)
abs_bucket_plus_co
Focal abs power + CO wavefront matching
pib_hard_tp
PIB maximization + quadratic TP (λ=10)
Most promising: PIB Only's 90% + TP enforcement
Future Directions
Dynamic D2NN
Sample-adaptive phase masks
Hybrid AO + D2NN
AO for low-order, D2NN for high-order
More Layers / Wider Aperture
Increase degrees of freedom
TV Weight Sweep
Optimize smoothness vs correction
Breaking the static limit requires moving beyond fixed phase masks