## Slide 1
Static D2NN vs MPLC
Atmospheric Turbulence Mitigation Approaches
Kim Lab | April 2026
Structural Similarity, Fundamental Differences

## Slide 2
Both Are Multi-Plane Phase Systems
SHARED ARCHITECTURE
Multiple phase-only masks + free-space propagation
Unitary transformation (energy conservation)
Cascaded Fourier / Fresnel transforms
Phase mask → Propagate → Phase mask → ...
Uₗ₊₁ = P_d { Uₗ · exp(iφₗ) }
KEY DIFFERENCE
MPLC: Analytically designed (wavefront matching algorithm)
D2NN: Data-driven training (stochastic gradient descent)
MPLC: Adaptive — different response per realization
D2NN: Static — same fixed mask for all inputs

## Slide 3
MPLC: Hermite-Gaussian Mode Decomposition
Uin(x,y) = Σ cn ψn(x,y) → MPLC separates each ψn to a different spatial port
Decomposes input into orthogonal HG/LG modes
Each mode sorted to separate spatial channel
Per-mode phase/amplitude measurement possible
Reconstruct corrected beam by selective recombination
Requires ADAPTIVE control for turbulence correction
Real-time mode sensing + feedback loop needed
Ref: Cailabs (commercial), Morizur et al. JOSA A 2010

## Slide 4
Our D2NN: Statistical Energy Redistribution
L = −log( E_bucket / E_input + ε )
Fixed (static) masks trained on turbulence ensemble
No mode decomposition — same transformation for ALL realizations
Optimizes ensemble-average received power in focal bucket
Mechanism: NOT wavefront correction (WF RMS unchanged at ~442nm)
Mechanism: PSF reshaping + deep fade floor lifting
PASSIVE — zero power consumption, no sensing required
Throughput preserved (0.88–0.996) without explicit penalty

## Slide 5
Head-to-Head Comparison
Aspect | MPLC (Adaptive) | Our D2NN (Static)
Design Method | Analytical (WFM) | Data-driven (SGD)
Operation | Mode decomposition | Energy redistribution
Adaptivity | Per-realization | Fixed mask
WF Correction | ✔ Yes (per mode) | ✘ No (WF RMS unchanged)
Turbulence Handling | Adaptive — real-time | Statistical — ensemble avg
Power Consumption | Active (sensing + control) | Zero (passive)
System Complexity | High (detector + SLM + FPGA) | Low (fixed diffractive element)
Performance | Full correction possible | +6% to +223% RP improvement
Fade Mitigation | Complete (adaptive) | Partial (8 dB at 3 km)
Cost | $$$ (SLM, detector, FPGA) | $ (fabricated once)

## Slide 6
Performance by Turbulence Regime
WEAK
D/r₀ < 2
MPLC
Near-perfect correction
Strehl → 1.0
D2NN
PSF reshaping
+91% RP (diffractive lens effect)
MODERATE
D/r₀ = 3–5
MPLC
Good correction
Limited by mode count
D2NN
"Correction gap"
Only +6–9% (static vs random)
STRONG
D/r₀ > 7
MPLC
Challenging
Scintillation limits sensing
D2NN
Surprisingly effective
+77% to +223% fade mitigation
D2NN excels where MPLC struggles (deep turbulence) and vice versa (moderate turbulence)

## Slide 7
What Should We Call This?
NOT "turbulence compensation"
No wavefront correction occurs
NOT "adaptive optics"
MORE ACCURATE TERMS
Turbulence-resilient passive beam shaping
Ensemble-optimized diffractive spatial filter
Static diffractive fade mitigation
Evidence | Supports "Mitigation"?
Received power +6–223% | ✔ Yes
Deep fades reduced by 8 dB | ✔ Yes
Zero power consumption | ✔ Yes
WF RMS unchanged (~442 nm) | ✘ No
No per-realization correction | ✘ No
Limited at moderate turbulence | ✘ No

## Slide 8
Complementary Hybrid: D2NN + MPLC
TURBULENT
BEAM
D2NN
(Passive Stage 1)
MPLC
(Active Stage 2)
CORRECTED
BEAM
▶
▶
▶
Why This Works
Reduced Dynamic Range
D2NN compresses fade depth → MPLC detector needs less dynamic range
Lower Update Rate
Pre-stabilized beam → MPLC can operate at slower refresh rate
Graceful Degradation
If MPLC fails, D2NN still provides baseline improvement
Cost Optimization
Simpler MPLC (fewer modes) needed after D2NN pre-conditioning

## Slide 9
Summary
1
D2NN and MPLC share the same architecture (multi-plane phase + propagation)
2
MPLC = adaptive mode decomposition; D2NN = static statistical optimization
3
D2NN is NOT turbulence "correction" — it's turbulence "resilience"
4
D2NN advantage: zero power, simple fabrication, effective in deep turbulence
5
MPLC advantage: true wavefront correction, full mode control
6
Future: D2NN (passive) + MPLC (active) hybrid could combine strengths